## Slide 1: Raster and Vector Datasets

## Slide 2: Vector model
Vertices
Polygon
Points
Nodes
Line
X
Y
Features are stored as a series of x-y coordinates in a rectangular coordinate system.
Many different coordinate systems may be used.

## Slide 3: Features linked to data
Each feature is linked to an entry in a data table containing information about the feature.

## Slide 4: Advantages of vectors
Precise location of features
Storing many attributes
Flexible for cartography
Compact storage of information
Ideally suited for certain types of analysis, especially areas, lengths, connections

## Slide 5: The Raster Data Model
The Raster Data Model is used to model spatial phenomena that vary continuously over a surface and that do not have discrete dimension
  Elevation
  Temperature
  Rainfall
  Noise Levels

## Slide 6: Surfaces Have Numeric Values
Things like elevation, temperature, slope and precipitation have measurable values for any particular location on the earth’s surface.

## Slide 7: The raster data model
Rows
Columns
X, Y location
Raster data file
N rows by M columns
X, Y location
Georeferenced to earth’s surface

## Slide 8: Digital Photos
The most familiar type of Raster Data is the digital photograph.
Digital Photos are raster datasets that record the relative amount of light being reflected off of a surface.

## Slide 9: Color Digital Photos
Color Digital Photos are actually made up of three Raster Datasets, each of which describes the amount of reflected Red, Green & Blue light, respectively.
These 3 raster datasets are combines (by the computer) into the R-G-B color image we are used to seeing.

## Slide 10: GIS data models
Vector model
Raster model

## Slide 11: Types of raster data
Discrete raster: land use
Continuous raster: DEM
Continuous raster: image
Discrete raster: roads

## Slide 12: Continuous data
Raster is the best way to store continuously changing values such as elevation
Analysis faster and more flexible than vectors for many applications
Some analysis only possible using rasters

## Slide 13: Raster analysis functions
Density
Least cost path
Distance
Interpolation
Viewshed
Buffers

## Slide 14: Impact of resolution
Storage space increases by the square of the resolution
Portraying large areas at high precision is problematic
90m resolution
10m resolution

## Slide 15: Storage of attributes
Roads may have other attributes: ownership, speed limit, number of lanes, etc.
Would need a new raster for each attribute
Only numeric attributes may be stored
Raster contains 1 value indicating a single attribute—road type for example

## Slide 17: Digital Raster Graphic

## Slide 18: Converting Vector to Raster Data is Easy

## Slide 19: Converting Raster Data to Vector is Hard Nearly Impossible

## Slide 20: Take a break for 10 minutes and we will meet again for laboratory work